BROWNTONE VOX

Water-Based Pigmented Sealer for Exposed Aggregate Concrete

{Note to Specifier: The paragraphs below are meant to be incorporated into Parts 2 and 3 of a standard CSI 3 Part Format specification, project’s General Structural Notes or directly onto the plans. They must be carefully reviewed by a qualified design professional and edited to meet the particular requirements of the project at hand, assure compliance with any governing building codes, and coordinate with other specification sections and drawings.}

PART 2:	PRODUCT

2.__CURING AND SEALING COMPOUND

A.	Concrete sealing compound. A ready-to-use, acrylic curing and sealer compound specially formulated with earth-toned pigments that highlight the natural color of the aggregate, making exposed aggregate surfaces look more even in color and richer in appearance. Although especially formulated for exposed aggregate concrete, BROWNTONE VOX can be used on any concrete surfaces - new or old - where a translucent brown tint is desired.

1. 	Product:

- Euclid Chemical Company (The): BrownTone VOX www.euclidchemical.com

2.__	Manufacturer shall have ISO 9001 Quality Certification.

PART 3: 	EXECUTION

3.__ 	EXAMINATION

A. 	When used on existing concrete, examine concrete surfaces to receive curing and sealing compound. Notify specifier if surfaces are not acceptable. Do not begin surface preparation or application until unacceptable conditions are corrected.

3.__	 SURFACE PREPARATION

A. 	When used on existing concrete, prepare concrete surfaces in accordance with manufacturer’s written instructions.

B. 	Ensure surfaces are clean and free of standing water.

C. 	Remove dirt, dust, oil, grease, sealers, and other materials that may prevent adhesion of sealing compound.

3.__ 	APPLICATION

A. 	Do not apply to concrete to receive toppings, epoxy coatings, urethane coatings, or epoxy adhesives.

B. 	Do not use as a bond breaker for tilt-up construction.

C. 	Do not dilute sealing compound.

D. 	Cure concrete surfaces as specified in Section 03300.